## Slide 1
COMPUTER NETWORKING
IPv4 & IPv6
Understanding Internet Protocols:
Addressing, Architecture & the Road Ahead
Suraj Kumar Jha | NCIT, Pokhara University

## Slide 2
WHY THIS TOPIC MATTERS
4.3B
Total IPv4
Addresses
All exhausted by 2011
340
Undecillion
IPv6 Address
Space
Essentially unlimited
45%+
Global IPv6
Adoption
Google stats, 2024
The internet is running out of IPv4 addresses — IPv6 is not optional, it's inevitable.

## Slide 3
What is IPv4?
Introduced in
1981 (RFC 791)
Address Size
32-bit
Format
Dotted Decimal
Example
192.168.1.1
Total Addresses
~4.3 Billion
Header Size
20–60 bytes (variable)
Address Breakdown
192
8 bits
168
8 bits
1
8 bits
1
8 bits
= 32 bits total
Address Classes
Class A: 0.0.0.0 – 127.x.x.x
Class B: 128.0.0.0 – 191.x.x.x
Class C: 192.0.0.0 – 223.x.x.x
D/E: Multicast / Research

## Slide 4
IPv4 Header Structure
Version
(4 bits)
IHL
(4 bits)
Type of Service
(8 bits)
Total Length
(16 bits)
Identification (16 bits)
Flags
(3)
Fragment Offset (13 bits)
TTL
(8 bits)
Protocol
(8 bits)
Header Checksum (16 bits)
Source IP Address (32 bits)
Destination IP Address (32 bits)
Key Fields:
TTL — Prevents infinite loops | Protocol — TCP=6, UDP=17 | Flags/Offset — Control fragmentation

## Slide 5
Limitations of IPv4
Address Exhaustion
IANA ran out of IPv4 blocks in February 2011. Regional registries have followed. NAT is a workaround — not a solution.
No Built-in Security
IPsec is optional in IPv4. Packets can be spoofed, intercepted, or modified without end-to-end encryption by default.
NAT Complexity
Network Address Translation breaks end-to-end connectivity, complicates peer-to-peer apps, and adds processing overhead.
Variable Header / Fragmentation
Routers must fragment packets, adding overhead. Options field makes the header variable-length, slowing routing.

## Slide 6
What is IPv6?
Introduced in
1998 (RFC 2460)
Address Size
128-bit
Format
Colon-Hex Notation
Example
2001:0db8::1
Total Addresses
340 Undecillion
Header Size
40 bytes (fixed)
Address Breakdown
2001
0db8
0000
0000
0000
0000
0000
0001
8 groups × 16 bits = 128 bits
Key Improvements Over IPv4
Mandatory IPsec
Auto-configuration (SLAAC)
No NAT needed
Multicast (no broadcast)
Simplified routing

## Slide 7
IPv6 Header Structure
Version
(4 bits)
Traffic Class
(8 bits)
Flow Label
(20 bits)
Payload Length (16 bits)
Next Header
(8 bits)
Hop Limit
(8 bits)
Source Address (128 bits)
Destination Address (128 bits)
IPv6 vs IPv4 Header — Key Simplifications
Fixed 40-byte header (no IHL field needed) No Header Checksum (handled by upper layers)
No Fragmentation at routers (done at source) Extension Headers replace IPv4 Options

## Slide 8
IPv4 vs IPv6 — Side by Side
Feature
IPv4
IPv6
Address Length
32 bits
128 bits
Address Format
Dotted Decimal
Colon Hexadecimal
Total Addresses
~4.3 Billion
340 Undecillion
Header Size
20–60 bytes (variable)
40 bytes (fixed)
Header Checksum
Yes
No (removed)
IPsec Support
Optional
Mandatory
Fragmentation
Routers & Source
Source only
Broadcast
Supported
Replaced by Multicast
NAT Required
Yes (address shortage)
No (vast address space)
Auto-configuration
DHCP (manual)
SLAAC (automatic)

## Slide 9
Transition Mechanisms
Dual Stack
Devices run both IPv4 and IPv6 simultaneously. Each packet is handled by the appropriate protocol. Most common approach used by ISPs and operating systems today.
Advantages:
Fully compatible
No tunneling overhead
Gradual rollout possible
Tunneling (6to4)
IPv6 packets are encapsulated inside IPv4 packets to cross IPv4 infrastructure. Enables IPv6 communication without upgrading the core network.
Advantages:
No core network change needed
Enables early IPv6 adoption
Transparent to end users
NAT-PT / Translation
Network Address Translation — Protocol Translation converts between IPv4 and IPv6 at the gateway level. Used when dual-stack or tunneling is not feasible.
Advantages:
Works with legacy IPv4 apps
No client modification needed
Useful at network edges

## Slide 10
IPv6 Adoption — Real World
Chart: IPv6 Adoption by Country (%, 2024)
| India | USA | Germany | France | Brazil | Japan | Nepal
IPv6 Adoption % | 71 | 53 | 64 | 60 | 35 | 47 | 8
45%+
Global Average
71%
India (highest)
8%
Nepal (growing)
2011
IANA IPv4 Exhaustion
Source: Google IPv6 Statistics, APNIC Labs, 2024

## Slide 11
Subnetting & CIDR
CIDR Notation
Classless Inter-Domain Routing (CIDR) replaces rigid class-based addressing. The prefix /n specifies how many bits are the network portion.
CIDR Block | Host Capacity | Subnet Mask
192.168.1.0/24 | 256 hosts | 255.255.255.0
10.0.0.0/8 | 16M hosts | 255.0.0.0
172.16.0.0/12 | 1M hosts | 255.240.0.0
192.168.1.0/26 | 64 hosts | 255.255.255.192
Subnet Calculation
Given:
192.168.1.0 /26
Network bits:
26
Host bits:
32 − 26 = 6
Hosts/subnet:
2⁶ − 2 = 62
Subnets:
2²⁶⁻²⁴ = 4
Block size:
256 − 192 = 64
Formula: Usable Hosts = 2ʰ − 2 (subtract network & broadcast)

## Slide 12
Key Takeaways
IPv4's 32-bit space is exhausted — ~4.3B addresses were not enough for the modern internet.
IPv6's 128-bit addressing solves this permanently with 340 undecillion unique addresses.
IPv6 improves security (mandatory IPsec), simplifies headers, and eliminates NAT.
Transition is gradual — Dual Stack, Tunneling, and NAT-PT bridge the two worlds.
Global adoption is rising (~45%), but many regions like Nepal are still in early stages.
"IPv6 is not the future — it's the present."

## Slide 13
Thank You &
Questions?
References
RFC 791 — Internet Protocol (IPv4), IETF, 1981
RFC 2460 — Internet Protocol Version 6, IETF, 1998
RFC 4291 — IPv6 Addressing Architecture
Google IPv6 Statistics — https://www.google.com/intl/en/ipv6/statistics.html
CN Lecture Notes — Yogesh Deo, NCIT