## Slide 1
DATA COMMUNICATION · CMP-335
Quadrature Amplitude
Modulation (QAM)
Suraj k. Jha
Roll No. 231537 · B.E. IT, 6th Semester
01

## Slide 4
01 · FOUNDATIONS
Modulation
Modulation is the process of modifying a carrier wave using a message signal to enable efficient transmission of information over a communication channel.
Why it matters
Baseband signals travel poorly over long distances — modulation shifts them onto a carrier suited to the channel.
Carrier, message, and resulting modulated waveform
02

## Slide 5
Quadrature
Quadrature is the condition where two signals of the same frequency are 90° out of phase with each other.
90°
phase offset between
the two carriers
I & Q
In-phase and Quadrature
components carried independently
Two carriers, same frequency, 90° apart
03

## Slide 6
02 · THE SCHEME
Quadrature Amplitude Modulation
QAM is a modulation scheme in which two carrier signals of the same frequency, separated by 90° in phase, are independently amplitude-modulated and combined to transmit information with high spectral efficiency.
IQ
Two orthogonal carriers
Uses two carrier signals: In-phase (I) and Quadrature (Q), modulated independently.
+
ASK + PSK combined
Combines the principles of Amplitude Shift Keying (ASK) and Phase Shift Keying (PSK).
↑
High efficiency
Provides high data rates and better bandwidth efficiency than simpler schemes.
04

## Slide 7
QAM Modulation Types
Higher-order QAM packs more bits per symbol at the cost of noise margin.
05

## Slide 8
03 · SYSTEM BLOCKS
QAM Modulator
A QAM modulator is a circuit that generates a QAM signal by modulating two orthogonal carrier signals (I and Q) with digital data and combining them for transmission.
1
Split data into I & Q streams
2
Modulate each onto orthogonal carriers
3
Sum the two for transmission
I/Q modulation and signal-combining stages
06

## Slide 9
QAM Demodulator
A QAM demodulator is a circuit that extracts the original digital data from a received QAM signal by separating the I and Q components.
⇄
Mirror of the modulator
It separates I and Q using synchronized reference carriers, then recombines them into the original bitstream.
Received signal separated back into I and Q data
07

## Slide 10
04 · ENCODING
Relationship Between Bits and Symbols
S
Symbol
A unique signal state used to represent one or more bits during transmission.
Instead of sending bits one by one, QAM groups multiple bits together and transmits them as a single symbol — multiplying effective throughput for the same symbol rate.
08

## Slide 11
Constellation Diagram
A graphical representation of digital modulation symbols, where each point represents a unique combination of amplitude and phase.
4-QAM
16-QAM
64-QAM
09

## Slide 12
Advantages of QAM
✓
High Data Rate
Transmits multiple bits per symbol, allowing faster data transmission.
✓
High Bandwidth Efficiency
Makes efficient use of available bandwidth within the same frequency range.
✓
High Spectral Efficiency
More data can be transmitted per unit of bandwidth than many other schemes.
✓
Flexible Modulation Orders
16-QAM, 64-QAM, 256-QAM and more can be selected based on channel conditions.
10

## Slide 13
Disadvantages of QAM
!
Sensitive to Noise
Higher-order QAM signals are more easily affected by noise and interference.
!
Requires High SNR
Reliable communication needs a strong and clean signal-to-noise ratio.
!
Complex Design
Modulators and demodulators are more complicated than simpler schemes.
!
Needs Precise Sync
Transmitter and receiver must maintain accurate carrier frequency and phase.
11

## Slide 14
05 · IN PRACTICE
Applications of Analog & Digital QAM
Analog QAM
Analog color television
Microwave communication
Analog radio systems
Analog video transmission
Digital QAM
Wi-Fi
4G LTE / 5G
Digital television
Cable TV & cable modems
Satellite communication
Broadband Internet
12